CALIBRATION CERTIFICATE
AT2327 Alarm Dosimeter	Date of calibration: $date

SN: $serial

Type: BDKN-02

Neutron flux density measurement limits: BDKN-02: 0.1 – 104 s-1·cm-2 ;

Measurement error: BDKN-02: ±20%

Operating conditions:
- Air temperature	+$temp °C
- Atmospheric pressure	98,5 kPa
- Relative humidity	$vlag %
- Gamma radiation background	$bground nSv/h

Calibration means:
$eng_facility_140;·

Calibration data

BDKN-02 (n) s/n: $bd_num1$
Flux density at check point φ0i , s-1·cm-2	Background / R=2,0 m	ИБН-8-3 / N027 / R=2,0 m / B(R)=0,600 / φ0i=5,9 / 1,0-10	ИБН-8-6 / N010 / R=2,0 m / B(R)=0,600 / φ0i=57,0 / 20-100	ИБН-8-6 / N010 / R=1,0 m / B(R)=0,863 / φ0i=235 / 2·102 - 103	ИБН-8-6 / N010 / R=0,5 m / B(R)=0,957 / φ0i=1019 / 2·103 - 104
Readings at check point φ0i, с-1·см-2 , %		$1-61 / $1-71 / $1-81	$1-62 / $1-72 / $1-82	$1-63 / $1-73 / $1-83	$1-64 / $1-74 / $1-84
Average readings, φi, s-1·cm-2	$1-00	$1-01	$1-02	$1-03	$1-04
Result of flux density measurement at control point / φnpi, s-1·cm-2		$1-n21	$1-n22	$1-n23	$1-n24
Intrinsic relative error of measurement, θпрi, %		$1-n31	$1-n32	$1-n33	$1-n34
Confidence limit of the intrinsic relative error Δi, %		$1-n41	$1-n42	$1-n43	$1-n44
Limite of intrinsic relative error , % not above		±20

Calibrated by:	$calibratedBy
		(signature)
Technical control:	$controlledBy
		(signature)