CALIBRATION CERTIFICATE
Type: Radiation monitor AT6130	Date of calibration: $date.

S/N: $allSerial

Measurement limits:
from 0.1 µSv/h to 10 mSv/h,
from 0.1 cps to 104 cps

Measurement error: ±20 %

Operating conditions:
- Air temperature	+$temp °C
- Atmospheric pressure	98,5 kPa
- Relative humidity	$vlag %
- Gamma radiation background	$bground nSv/h

Calibration means:
- $eng_facility_110$;
- $eng_facility_130$;
- $eng_facility_beta$.

Calibration data

Gamma radiation, 137Cs
Radiation monitor AT6130 S/N $bd_num1$
Dose rate at check point Ḣoi(10)	Radia-tion source number	Distan-ce to source, / R, сm	Dose rate measurement at check point,					Relative gamma radiation measurement error, θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, % / not above
			Back-ground, nSv/h	Measured value Ḣ*i(10)			Average value, Hi(10)
				H1	H2	H3
0,7 µSv/h	$1-30	$1-40	$1-50	$1-60	$1-70	$1-80	$1-00	$1-10	$1-20	±20
7 µSv/h	$1-31	$1-41	$1-51	$1-61	$1-71	$1-81	$1-01	$1-11	$1-21
70 µSv/h	$1-32	$1-42	$1-52	$1-62	$1-72	$1-82	$1-02	$1-12	$1-22
0.7 mSv/h	$1-33	$1-43	$1-53	$1-63	$1-73	$1-83	$1-03	$1-13	$1-23
7,0 mSv/h	$1-34	$1-44	$1-54	$1-64	$1-74	$1-84	$1-04	$1-14	$1-24

Beta radiation, Sr-90+Y-90, area source 160 mm2
Radiation monitor AT6130 S/N $bd_num_b1$
Conventionally true value of external solid angle radiation 2πav, cps	Radiation source number	Count rate in test point				Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, % / not above
		Measured value, cps			Average value, cps
		cps1	cps2	cps3
β1-90	0660	β1-60	β1-70	β1-80	β1-00	β1-10	β1-20	±20
β1-91	6905	β1-61	β1-71	β1-81	β1-01	β1-11	β1-21
β1-92	0661	β1-62	β1-72	β1-82	β1-02	β1-12	β1-22
β1-93	0662	β1-63	β1-73	β1-83	β1-03	β1-13	β1-23

Calibrated by:	$calibratedBy
		(signature)
Technical control:	$controlledBy
		(signature)