CALIBRATION CERTIFICATE

Type: Personal dosimeter AT3509	Date of calibration: $date

S/n: $allSerial

Measurement limits:
0.1 µSv/h – 1.0 Sv/h

Measurement error:
0.1 µSv/h – 0.99 µSv/h – ±30%,
1 µSv/h – 1 Sv/h – ±15%

Operating conditions:
- Air temperature	+$temp °C
- Atmospheric pressure	98,5 kPa
- Relative humidity	$vlag %
- Gamma radiation background	$bground nSv/h

$facility_13+11eng;

Calibration data:
AT3509 (γ) s/n: $bd_num1$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$1-d0		$1-av-bg	---	---	---	---
0.80 µSv/h	$1-n0	$1-d0		$1-av0	$1-o0	$1-q0	$1-do0	±30
4.0 mSv/h	$1-n1	$1-d1		$1-av1	$1-o1	$1-q1	$1-do1	±15
800.0 mSv/h	$1-n2	$1-d2		$1-av2	$1-o2	$1-q2	$1-do2	±15

AT3509 (γ) s/n: $bd_num1$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$1-dn_3	$1-dd_3 / 360s	$1-d_dev_3	$1-dose_3	$1-d_res_3	$1-o_pog_3	$1-d_gran_3	±15
4.0 mSv/h	$1-dn	$1-dd / 180s	$1-d_dev	$1-dose	$1-d_res	$1-o_pog	$1-d_gran	±15

AT3509 (γ) s/n: $bd_num2$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$2-d0		$2-av-bg	---	---	---	---
0.80 µSv/h	$2-n0	$2-d0		$2-av0	$2-o0	$2-q0	$2-do0	±30
4.0 mSv/h	$2-n1	$2-d1		$2-av1	$2-o1	$2-q1	$2-do1	±15
800.0 mSv/h	$2-n2	$2-d2		$2-av2	$2-o2	$2-q2	$2-do2	±15

AT3509 (γ) s/n: $bd_num2$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$2-dn_3	$2-dd_3 / 360s	$2-d_dev_3	$2-dose_3	$2-d_res_3	$2-o_pog_3	$2-d_gran_3	±15
4.0 mSv/h	$2-dn	$2-dd / 180s	$2-d_dev	$2-dose	$2-d_res	$2-o_pog	$2-d_gran	±15

AT3509 (γ) s/n: $bd_num3$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$3-d0		$3-av-bg	---	---	---	---
0.80 µSv/h	$3-n0	$3-d0		$3-av0	$3-o0	$3-q0	$3-do0	±30
4.0 mSv/h	$3-n1	$3-d1		$3-av1	$3-o1	$3-q1	$3-do1	±15
800.0 mSv/h	$3-n2	$3-d2		$3-av2	$3-o2	$3-q2	$3-do2	±15

AT3509 (γ) s/n: $bd_num3$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$3-dn_3	$3-dd_3 / 360s	$3-d_dev_3	$3-dose_3	$3-d_res_3	$3-o_pog_3	$3-d_gran_3	±15
4.0 mSv/h	$3-dn	$3-dd / 180s	$3-d_dev	$3-dose	$3-d_res	$3-o_pog	$3-d_gran	±15

AT3509 (γ) s/n: $bd_num4$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$4-d0		$4-av-bg	---	---	---	---
0.80 µSv/h	$4-n0	$4-d0		$4-av0	$4-o0	$4-q0	$4-do0	±30
4.0 mSv/h	$4-n1	$4-d1		$4-av1	$4-o1	$4-q1	$4-do1	±15
800.0 mSv/h	$4-n2	$4-d2		$4-av2	$4-o2	$4-q2	$4-do2	±15

AT3509 (γ) s/n: $bd_num4$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$4-dn_3	$4-dd_3 / 360s	$4-d_dev_3	$4-dose_3	$4-d_res_3	$4-o_pog_3	$4-d_gran_3	±15
4.0 mSv/h	$4-dn	$4-dd / 180s	$4-d_dev	$4-dose	$4-d_res	$4-o_pog	$4-d_gran	±15

AT3509 (γ) s/n: $bd_num5$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$5-d0		$5-av-bg	---	---	---	---
0.80 µSv/h	$5-n0	$5-d0		$5-av0	$5-o0	$5-q0	$5-do0	±30
4.0 mSv/h	$5-n1	$5-d1		$5-av1	$5-o1	$5-q1	$5-do1	±15
800.0 mSv/h	$5-n2	$5-d2		$5-av2	$5-o2	$5-q2	$5-do2	±15

AT3509 (γ) s/n: $bd_num5$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$5-dn_3	$5-dd_3 / 360s	$5-d_dev_3	$5-dose_3	$5-d_res_3	$5-o_pog_3	$5-d_gran_3	±15
4.0 mSv/h	$5-dn	$5-dd / 180s	$5-d_dev	$5-dose	$5-d_res	$5-o_pog	$5-d_gran	±15

AT3509 (γ) s/n: $bd_num6$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$6-d0		$6-av-bg	---	---	---	---
0.80 µSv/h	$6-n0	$6-d0		$6-av0	$6-o0	$6-q0	$6-do0	±30
4.0 mSv/h	$6-n1	$6-d1		$6-av1	$6-o1	$6-q1	$6-do1	±15
800.0 mSv/h	$6-n2	$6-d2		$6-av2	$6-o2	$6-q2	$6-do2	±15

AT3509 (γ) s/n: $bd_num6$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$6-dn_3	$6-dd_3 / 360s	$6-d_dev_3	$6-dose_3	$6-d_res_3	$6-o_pog_3	$6-d_gran_3	±15
4.0 mSv/h	$6-dn	$6-dd / 180s	$6-d_dev	$6-dose	$6-d_res	$6-o_pog	$6-d_gran	±15

AT3509 (γ) s/n: $bd_num7$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$7-d0		$7-av-bg	---	---	---	---
0.80 µSv/h	$7-n0	$7-d0		$7-av0	$7-o0	$7-q0	$7-do0	±30
4.0 mSv/h	$7-n1	$7-d1		$7-av1	$7-o1	$7-q1	$7-do1	±15
800.0 mSv/h	$7-n2	$7-d2		$7-av2	$7-o2	$7-q2	$7-do2	±15

AT3509 (γ) s/n: $bd_num7$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$7-dn_3	$7-dd_3 / 360s	$7-d_dev_3	$7-dose_3	$7-d_res_3	$7-o_pog_3	$7-d_gran_3	±15
4.0 mSv/h	$7-dn	$7-dd / 180s	$7-d_dev	$7-dose	$7-d_res	$7-o_pog	$7-d_gran	±15

AT3509 (γ) s/n: $bd_num8$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$8-d0		$8-av-bg	---	---	---	---
0.80 µSv/h	$8-n0	$8-d0		$8-av0	$8-o0	$8-q0	$8-do0	±30
4.0 mSv/h	$8-n1	$8-d1		$8-av1	$8-o1	$8-q1	$8-do1	±15
800.0 mSv/h	$8-n2	$8-d2		$8-av2	$8-o2	$8-q2	$8-do2	±15

AT3509 (γ) s/n: $bd_num8$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$8-dn_3	$8-dd_3 / 360s	$8-d_dev_3	$8-dose_3	$8-d_res_3	$8-o_pog_3	$8-d_gran_3	±15
4.0 mSv/h	$8-dn	$8-dd / 180s	$8-d_dev	$8-dose	$8-d_res	$8-o_pog	$8-d_gran	±15

AT3509 (γ) s/n: $bd_num9$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$9-d0		$9-av-bg	---	---	---	---
0.80 µSv/h	$9-n0	$9-d0		$9-av0	$9-o0	$9-q0	$9-do0	±30
4.0 mSv/h	$9-n1	$9-d1		$9-av1	$9-o1	$9-q1	$9-do1	±15
800.0 mSv/h	$9-n2	$9-d2		$9-av2	$9-o2	$9-q2	$9-do2	±15

AT3509 (γ) s/n: $bd_num9$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$9-dn_3	$9-dd_3 / 360s	$9-d_dev_3	$9-dose_3	$9-d_res_3	$9-o_pog_3	$9-d_gran_3	±15
4.0 mSv/h	$9-dn	$9-dd / 180s	$9-d_dev	$9-dose	$9-d_res	$9-o_pog	$9-d_gran	±15

AT3509 (γ) s/n: $bd_num10$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$10-d0		$10-av-bg	---	---	---	---
0.80 µSv/h	$10-n0	$10-d0		$10-av0	$10-o0	$10-q0	$10-do0	±30
4.0 mSv/h	$10-n1	$10-d1		$10-av1	$10-o1	$10-q1	$10-do1	±15
800.0 mSv/h	$10-n2	$10-d2		$10-av2	$10-o2	$10-q2	$10-do2	±15

AT3509 (γ) s/n: $bd_num10$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$10-dn_3	$10-dd_3 / 360s	$10-d_dev_3	$10-dose_3	$10-d_res_3	$10-o_pog_3	$10-d_gran_3	±15
4.0 mSv/h	$10-dn	$10-dd / 180s	$10-d_dev	$10-dose	$10-d_res	$10-o_pog	$10-d_gran	±15

AT3509 (γ) s/n: $bd_num11$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$11-d0		$11-av-bg	---	---	---	---
0.80 µSv/h	$11-n0	$11-d0		$11-av0	$11-o0	$11-q0	$11-do0	±30
4.0 mSv/h	$11-n1	$11-d1		$11-av1	$11-o1	$11-q1	$11-do1	±15
800.0 mSv/h	$11-n2	$11-d2		$11-av2	$11-o2	$11-q2	$11-do2	±15

AT3509 (γ) s/n: $bd_num11$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$11-dn_3	$11-dd_3 / 360s	$11-d_dev_3	$11-dose_3	$11-d_res_3	$11-o_pog_3	$11-d_gran_3	±15
4.0 mSv/h	$11-dn	$11-dd / 180s	$11-d_dev	$11-dose	$11-d_res	$11-o_pog	$11-d_gran	±15

AT3509 (γ) s/n: $bd_num12$
Dose rate at check point, / Ḣoi(10)	Radia-tion source number	Distance to source, / R, сm	Dose rate measurement at check point, / Ḣ*i(10)	Average value, / Hpi(10)	Relative measure-ment error / θпрi, %	Relative standard deviation, / Si, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative / error, % / not above
Background	---	$12-d0		$12-av-bg	---	---	---	---
0.80 µSv/h	$12-n0	$12-d0		$12-av0	$12-o0	$12-q0	$12-do0	±30
4.0 mSv/h	$12-n1	$12-d1		$12-av1	$12-o1	$12-q1	$12-do1	±15
800.0 mSv/h	$12-n2	$12-d2		$12-av2	$12-o2	$12-q2	$12-do2	±15

AT3509 (γ) s/n: $bd_num12$
Actual dose value, / Hp0(10)	Radiation source number	d, cm / t, s	Measured dose value			Relative measure-ment error / θпрi, %	Confidence limit of the intrinsic relative error Δi, %	Limits of intrinsic relative error, / % / not above
			Hpi(10)	Hpi(10)meas.	Hpi(10)meas.-Hp0(10)
4.0 µSv/h	$12-dn_3	$12-dd_3 / 360s	$12-d_dev_3	$12-dose_3	$12-d_res_3	$12-o_pog_3	$12-d_gran_3	±15
4.0 mSv/h	$12-dn	$12-dd / 180s	$12-d_dev	$12-dose	$12-d_res	$12-o_pog	$12-d_gran	±15

Calibrated by:	$calibratedBy
		(signature)
Technical control:	$controlledBy
		(signature)